## Slide 1: ICTNWK541 Assessment
Assessment Task 2: Project Portfolio Manuel Sergio Perez Espitia

## Slide 2
ABC Enterprises is a growing business based in Melbourne with two branches in Sydney and Brisbane.

## Slide 3
ABC Enterprises wants to improve its network due to old infrastructure, security and reliability WAN connectivity between Sydney Branch and Brisbane Branch. We are the network engineer responsible for implementing the required WAN connectivity for ABC Enterprises.

## Slide 4
This is Sydney Branch

## Slide 5
This is Brisbane Branch

## Slide 6
I am going to use this simulation software and tools

## Slide 7
Network details for both branches
Both are a dual-star, high-availability, that use Ethernet connections, only in Brisbane Branch uses Coax and phone Lines connections. Sydney is a 3-tier and Brisbane is a 2-tier network

## Slide 9
I gonna cover these topics
I have included “WAN Configuration and Troubleshooting & Testing” together to show their results

## Slide 11
I designed some policies that fit the project requirements.

## Slide 12
If the network is attacked with sniffing, this prevents the data from being seen in clear format.

## Slide 13
prevents unauthorised users from using computer systems

## Slide 14
protects data travelling on the Internet

## Slide 15
helps prevent attacks from outside the network

## Slide 16
only allows authorised users access to infrastructure devices

## Slide 18
It implements a dual-stack with a DHCP-router to avoid having dedicated servers. Redundancy is provided by LACP on the switches and HSRP (only Sydney) on the routers. Additionally, LACP provides three communication lanes to increase bandwidth. Communication between LAN networks over internet is provided by OSPF.
DHCP-router

## Slide 19
For simplicity I am going to only show the tests in IPv4 or Ipv6, show both it will take too long time, all the tests are in the document

## Slide 20
Testing local network connection over IPv6

## Slide 21
Connection to its WEB server

## Slide 24
Brisbane Branch is the only one that has DSL implementation, this is the blue area and works with two modems

## Slide 25
Now, this is the test for local network connection over IPv4

## Slide 26
In the blue area After implement VPN this connection is no longer available, I could not fixed it.
the rest of the network is working

## Slide 27
Now, those are the WAN test results

## Slide 28
From Sydney to Brisbane over IPv4

## Slide 29
From Brisbane to Sydney over IPv6

## Slide 30
Secure remote access by login on network devices
Implemented on routers and switches

## Slide 34
I have implemented a DHCP-router to avoid having dedicated servers.

## Slide 37
I have implemented LACP to combines 3 links into a logical connection because I am also using a second switch layer 3 to redundancy on each sub-network.

## Slide 41
I have implemented HSRP on Sydney Branch to provide local redundancy

## Slide 45
I have implemented OSPF to have dynamic routing between both branches

## Slide 50
Rules that I have implemented them for allowing traffic among Sydney and Brisbane Branches networks."

## Slide 53
I have implemented VPN with IPsec protocol to Create a secure network over the Internet between protecting data confidentiality and integrity.

## Slide 56
My network doesn't support PPP because the WAN connections are Ethernet. PPP requires serial connections. Additionally, PPP isn't compatible with HSRP.
So I used the reference network given in class.

## Slide 57
I have Implemented CHAP as an automatic authentication method.

## Slide 59
Dynamic NAT were performed on the file shared in class due to extra complexity over my network.

## Slide 63
Also, Firewall and single-port tests were performed on the file submitted in class due to extra complexity over my network.

## Slide 69
I have created a sheet with a brief explanation of the technologies I have used.

## Slide 75
Mainly the information I have used has been from these web sources

## Slide 76: END
THANKS!